Experiment 2

20th February 2019

Aim:	To learn to set up a complete network interface by configuring	services such as gateway, DNS, IP tables etc. using ifconfig.

---------------------------------------------------------------------------------------------
---------------------------------------------------------------------------------------------

1. ifconfig : it is used to configure kernel-resident network interfaces. It is used at boot time to configure as necessary. After that it is used when debugging or system tuning is required.

1.1 ifconfig -a : used to display all the interfaces even if they are currently unavailable.

Example usage:

ifconfig <flags> <interface>

Terminal===================================================

##Using the ifconfig to view all adapters

[protonegative@fedora ~]$ ifconfig
enp7s0: flags=4099<UP,BROADCAST,MULTICAST> mtu 1500
        ether 20:47:47:bd:81:d8 txqueuelen 1000 (Ethernet)
        RX packets 0 bytes 0 (0.0 B)
        RX errors 0 dropped 0 overruns 0 frame 0
        TX packets 0 bytes 0 (0.0 B)
        TX errors 0 dropped 0 overruns 0 carrier 0 collisions 0

lo: flags=73<UP,LOOPBACK,RUNNING> mtu 65536
        inet 127.0.0.1 netmask 255.0.0.0
        inet6 ::1 prefixlen 128 scopeid 0x10<host>
        loop txqueuelen 1000 (Local Loopback)
        RX packets 5068 bytes 1033314 (1009.0 KiB)
        RX errors 0 dropped 0 overruns 0 frame 0
        TX packets 5068 bytes 1033314 (1009.0 KiB)
        TX errors 0 dropped 0 overruns 0 carrier 0 collisions 0

wlp6s0: flags=4163<UP,BROADCAST,RUNNING,MULTICAST> mtu 1500
        inet 192.168.43.31 netmask 255.255.255.0 broadcast 192.168.43.255
        inet6 fe80::e6f2:5164:15be:9642 prefixlen 64 scopeid 0x20<link>
        ether e4:f8:9c:aa:d9:49 txqueuelen 1000 (Ethernet)
        RX packets 468584 bytes 523733332 (499.4 MiB)
        RX errors 0 dropped 0 overruns 0 frame 0
        TX packets 282870 bytes 41834086 (39.8 MiB)
        TX errors 0 dropped 0 overruns 0 carrier 0 collisions 0

##View a specific adapter

[protonegative@fedora ~]$ ifconfig wlp6s0
wlp6s0: flags=4163<UP,BROADCAST,RUNNING,MULTICAST> mtu 1500
        inet 192.168.43.31 netmask 255.255.255.0 broadcast 192.168.43.255
        inet6 fe80::e6f2:5164:15be:9642 prefixlen 64 scopeid 0x20<link>
        ether e4:f8:9c:aa:d9:49 txqueuelen 1000 (Ethernet)
        RX packets 468632 bytes 523740915 (499.4 MiB)
        RX errors 0 dropped 0 overruns 0 frame 0
        TX packets 282922 bytes 41842725 (39.9 MiB)
        TX errors 0 dropped 0 overruns 0 carrier 0 collisions 0

##To turn an adapter on or off
[protonegative@fedora ~]$ sudo ifconfig enp7s0 down
[sudo] password for protonegative:
[protonegative@fedora ~]$ sudo ifconfig enp7s0 up

========================================================end

2. route : it is used to manipulate the kernel’s routing tables. Its primary use is to set up static routes to specific hosts or networks via an interface after it has been configured with the ifconfig program.

Example usage:

route <flags>
route <flags> add <target>
route <flags> del <target>

Terminal===================================================

##Checking default gateways

[protonegative@fedora ~]$ route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
default gateway 0.0.0.0 UG 600 0 0 wlp6s0
192.168.43.0 0.0.0.0 255.255.255.0 U 600 0 0 wlp6s0

##Deleting routes

[protonegative@fedora ~]$ sudo route delete default gw <IP Address> <Adaptor>

##Adding routes

[protonegative@fedora ~]$ sudo route add default gw <IP Adress> <Adaptor>

========================================================end

3. Changing DNS settings: If our DNS settings are misconfigured or preferred we can change it adding a name server into the ‘resolve.conf’ located in ‘/etc’

Example Usage:

Terminal===================================================

##Adding a DNS server to resolv.conf

[protonegative@fedora ~]$ sudo echo “nameserver <IPv4/IPv6 addr>” >> /etc/resolv.conf

##To get IPv6 addr

[protonegative@fedora ~]$ host `host <IPv4 addr> | awk {'print $5'} | sed 's/.$//'` | grep IPv6 | awk {'print $5'}

##This addr can be added to resolv.conf in the same way

##Restart NetworkManager after making changes

[protonegative@fedora ~]$ service NetworkManager restart

========================================================end

4. iptables: are used to set up, maintain and inspect the tables of IPv4 and IPv6 packet filter rules in the Linux kernel.

Example Usage:

Terminal===================================================

##To get a numerical list of our iptable rules

[protonegative@fedora ~]$ sudo iptables -L -nv --line-numbers
Chain INPUT (policy ACCEPT 0 packets, 0 bytes)
num pkts bytes target prot opt in out source destination
1 384K 514M ACCEPT all -- * * 0.0.0.0/0 0.0.0.0/0 ctstate RELATED,ESTABLISHED
2 2819 193K ACCEPT all -- lo * 0.0.0.0/0 0.0.0.0/0
3 2891 394K INPUT_direct all -- * * 0.0.0.0/0 0.0.0.0/0
4 2891 394K INPUT_ZONES_SOURCE all -- * * 0.0.0.0/0 0.0.0.0/0
5 2891 394K INPUT_ZONES all -- * * 0.0.0.0/0 0.0.0.0/0
6 3 219 DROP all -- * * 0.0.0.0/0 0.0.0.0/0 ctstate INVALID
7 11 3249 REJECT all -- * * 0.0.0.0/0 0.0.0.0/0 reject-with icmp-host-prohibited

Chain FORWARD (policy ACCEPT 0 packets, 0 bytes)
num pkts bytes target prot opt in out source destination
1 0 0 ACCEPT all -- * * 0.0.0.0/0 0.0.0.0/0 ctstate RELATED,ESTABLISHED
2 0 0 ACCEPT all -- lo * 0.0.0.0/0 0.0.0.0/0
3 0 0 FORWARD_direct all -- * * 0.0.0.0/0 0.0.0.0/0
4 0 0 FORWARD_IN_ZONES_SOURCE all -- * * 0.0.0.0/0 0.0.0.0/0
5 0 0 FORWARD_IN_ZONES all -- * * 0.0.0.0/0 0.0.0.0/0
6 0 0 FORWARD_OUT_ZONES_SOURCE all -- * * 0.0.0.0/0 0.0.0.0/0
7 0 0 FORWARD_OUT_ZONES all -- * * 0.0.0.0/0 0.0.0.0/0
8 0 0 DROP all -- * * 0.0.0.0/0 0.0.0.0/0 ctstate INVALID
9 0 0 REJECT all -- * * 0.0.0.0/0 0.0.0.0/0 reject-with icmp-host-prohibited

Chain OUTPUT (policy ACCEPT 46787 packets, 6203K bytes)
num pkts bytes target prot opt in out source destination
1 285K 31M OUTPUT_direct all -- * * 0.0.0.0/0 0.0.0.0/0

Chain FORWARD_IN_ZONES (1 references)
num pkts bytes target prot opt in out source destination
1 0 0 FWDI_FedoraWorkstation all -- wlp6s0 * 0.0.0.0/0 0.0.0.0/0 [goto]
2 0 0 FWDI_FedoraWorkstation all -- + * 0.0.0.0/0 0.0.0.0/0 [goto]

Chain FORWARD_IN_ZONES_SOURCE (1 references)
num pkts bytes target prot opt in out source destination

Chain FORWARD_OUT_ZONES (1 references)
num pkts bytes target prot opt in out source destination
1 0 0 FWDO_FedoraWorkstation all -- * wlp6s0 0.0.0.0/0 0.0.0.0/0 [goto]
2 0 0 FWDO_FedoraWorkstation all -- * + 0.0.0.0/0 0.0.0.0/0 [goto]

Chain FORWARD_OUT_ZONES_SOURCE (1 references)
num pkts bytes target prot opt in out source destination

Chain FORWARD_direct (1 references)
num pkts bytes target prot opt in out source destination

Chain FWDI_FedoraWorkstation (2 references)
num pkts bytes target prot opt in out source destination
1 0 0 FWDI_FedoraWorkstation_log all -- * * 0.0.0.0/0 0.0.0.0/0
2 0 0 FWDI_FedoraWorkstation_deny all -- * * 0.0.0.0/0 0.0.0.0/0
3 0 0 FWDI_FedoraWorkstation_allow all -- * * 0.0.0.0/0 0.0.0.0/0
4 0 0 ACCEPT icmp -- * * 0.0.0.0/0 0.0.0.0/0

Chain FWDI_FedoraWorkstation_allow (1 references)
num pkts bytes target prot opt in out source destination

Chain FWDI_FedoraWorkstation_deny (1 references)
num pkts bytes target prot opt in out source destination

Chain FWDI_FedoraWorkstation_log (1 references)
num pkts bytes target prot opt in out source destination

Chain FWDO_FedoraWorkstation (2 references)
num pkts bytes target prot opt in out source destination
1 0 0 FWDO_FedoraWorkstation_log all -- * * 0.0.0.0/0 0.0.0.0/0
2 0 0 FWDO_FedoraWorkstation_deny all -- * * 0.0.0.0/0 0.0.0.0/0
3 0 0 FWDO_FedoraWorkstation_allow all -- * * 0.0.0.0/0 0.0.0.0/0

Chain FWDO_FedoraWorkstation_allow (1 references)
num pkts bytes target prot opt in out source destination

Chain FWDO_FedoraWorkstation_deny (1 references)
num pkts bytes target prot opt in out source destination

Chain FWDO_FedoraWorkstation_log (1 references)
num pkts bytes target prot opt in out source destination

Chain INPUT_ZONES (1 references)
num pkts bytes target prot opt in out source destination
1 623 85864 IN_FedoraWorkstation all -- wlp6s0 * 0.0.0.0/0 0.0.0.0/0 [goto]
2 0 0 IN_FedoraWorkstation all -- + * 0.0.0.0/0 0.0.0.0/0 [goto]

Chain INPUT_ZONES_SOURCE (1 references)
num pkts bytes target prot opt in out source destination

Chain INPUT_direct (1 references)
num pkts bytes target prot opt in out source destination

Chain IN_FedoraWorkstation (2 references)
num pkts bytes target prot opt in out source destination
1 2891 394K IN_FedoraWorkstation_log all -- * * 0.0.0.0/0 0.0.0.0/0
2 2891 394K IN_FedoraWorkstation_deny all -- * * 0.0.0.0/0 0.0.0.0/0
3 2891 394K IN_FedoraWorkstation_allow all -- * * 0.0.0.0/0 0.0.0.0/0
4 0 0 ACCEPT icmp -- * * 0.0.0.0/0 0.0.0.0/0

Chain IN_FedoraWorkstation_allow (1 references)
num pkts bytes target prot opt in out source destination
1 0 0 ACCEPT tcp -- * * 0.0.0.0/0 0.0.0.0/0 tcp dpt:22 ctstate NEW
2 34 2940 ACCEPT udp -- * * 0.0.0.0/0 0.0.0.0/0 udp dpt:137 ctstate NEW
3 5 1085 ACCEPT udp -- * * 0.0.0.0/0 0.0.0.0/0 udp dpt:138 ctstate NEW
4 182 21771 ACCEPT udp -- * * 0.0.0.0/0 224.0.0.251 udp dpt:5353 ctstate NEW
5 2653 364K ACCEPT udp -- * * 0.0.0.0/0 0.0.0.0/0 udp dpts:1025:65535 ctstate NEW
6 3 345 ACCEPT tcp -- * * 0.0.0.0/0 0.0.0.0/0 tcp dpts:1025:65535 ctstate NEW

Chain IN_FedoraWorkstation_deny (1 references)
num pkts bytes target prot opt in out source destination

Chain IN_FedoraWorkstation_log (1 references)
num pkts bytes target prot opt in out source destination

Chain OUTPUT_direct (1 references)
num pkts bytes target prot opt in out source destination

##Example to Accept incoming connections over port ##8080(TCP)

[protonegative@fedora ~]$ sudo iptables -I INPUT 7 -p tcp --dport 8080 -m state --state NEW -j ACCEPT

##Example to replace to rule

[protonegative@fedora ~]$ sudo iptables -R INPUT 9 -m limit --limit 3/min -j LOG --log-prefix "iptables_INPUT_denied: " --log-level 7

##Example to delete a rule

[protonegative@fedora ~]$ sudo iptables -D INPUT 7

========================================================end

5. iwconfig: it is similar to ifconfig but is specific to wireless adapters.

Example Usage:

iwconfig <flags> <interface> <mode> <state>

Terminal===================================================

##View Details of wireless extensions

[protonegative@fedora ~]$ iwconfig
wlp6s0 IEEE 802.11 ESSID:"connect"
        Mode:Managed Frequency:2.412 GHz Access Point: 4A:FC:B6:76:4D:E2
        Bit Rate=72.2 Mb/s Tx-Power=20 dBm
        Retry short limit:7 RTS thr:off Fragment thr:off
        Power Management:on
        Link Quality=55/70 Signal level=-55 dBm
        Rx invalid nwid:0 Rx invalid crypt:0 Rx invalid frag:0
        Tx excessive retries:5 Invalid misc:699 Missed beacon:0

enp7s0 no wireless extensions.

lo no wireless extensions.

##To change the mode of the wireless interface

[protonegative@fedora ~]$ iwconfig wlp6s0 mode monitor

========================================================end

Result: Understood the usage of certain network managing commands

---------------------------------------------------------------------------------------------
       eof
---------------------------------------------------------------------------------------------